## Slide 1: Pipelining and Hazards
Instructor: Rebecca Herman

## Slide 2: Great Idea #4: Parallelism
Parallel Requests
  Assigned to computer
  e.g. search “Garcia”
Parallel Threads
  Assigned to core
  e.g. lookup, ads
Parallel Instructions
  > 1 instruction @ one time
  e.g. 5 pipelined instructions
Parallel Data
  > 1 data item @ one time
  e.g. add of 4 pairs of words
Hardware descriptions
  All gates functioning in parallel at same time
Smart Phone
Warehouse Scale Computer
Leverage Parallelism &
Achieve High Performance
Core
…
Memory
Input/Output
Computer
Core
Software Hardware
Cache Memory
Core
Instruction Unit(s)
Functional
Unit(s)
A0+B0
A1+B1
A2+B2
A3+B3
Logic Gates

## Slide 3: Review of Last Lecture
Implementing controller for your datapath
  Take decoded signals from instruction and generate control signals
Pipelining improves performance by exploiting Instruction Level Parallelism
  5-stage pipeline for MIPS: IF, ID, EX, MEM, WB
  Executes multiple instructions in parallel
  Each instruction has the same latency
  What can go wrong???

## Slide 4: Pipelined Datapath
Add registers between stages
  Hold information produced in previous cycle
5 stage pipeline
  Clock rate potentially 5x faster
1. Instruction
Fetch
2. Decode/
Register Read
3. Execute
4. Memory
5. Register
Write
PC
instruction
memory
+4
Register
File
rt
rs
rd
ALU
Data
memory
imm
MUX

## Slide 5: Measurements of Performance
Latency (or response time or execution time)
  Time to complete one task (#stages * Tclk)
Bandwidth (or throughput)
  Tasks completed per unit time (#stages/latency)
Example: clk-to-q: 10ms, setup 5ms, add 110ms, shift: 75ms
TCLK =
200ms
TCLK =
125ms
Latency? Throughput?
200ms 1/200ms
+ tCLK-to-Q = 5 tasks/sec
Latency? Throughput?
2*125ms 1/125ms
+ tCLK-to-Q = 8 tasks/sec

## Slide 6: Pipelined Datapath (Detailed)

## Slide 7: Graphical Pipeline Representation
I
n
s
t
r
O
r
d
e
r
Load
Add
Store
Sub
Or
I$
Time (clock cycles)
I$
ALU
Reg
Reg
I$
D$
ALU
ALU
Reg
D$
Reg
I$
D$
Reg
ALU
Reg
Reg
Reg
D$
Reg
D$
ALU
RegFile: right half is read, left half is write
Reg
I$

## Slide 8
Question: Which of the following signals (buses or control signals) for MIPS-lite does NOT need to be passed into the EX pipeline stage?
Beq
(A)
MemWr
(B)
RegWr
(C)
imm16
(D)
IF
ID
EX
Mem
WB
ALU
I$
Reg
D$
Reg

## Slide 9: Hazards Ahead!

## Slide 10: Pipelining Hazards
A hazard is a situation that prevents starting the next instruction in the next clock cycle
Structural hazard
  A required resource is busy (e.g. needed in multiple stages)
Data hazard
  Data dependency between instructions
  Need to wait for previous instruction to complete its data write
Control hazard
  Flow of execution depends on previous instruction

## Slide 11: Agenda
Structural Hazards
Data Hazards
  Forwarding
Administrivia
Data Hazards (Continued)
  Load Delay Slot
Control Hazards
  Branch and Jump Delay Slots
  Branch Prediction

## Slide 12: 1. Structural Hazards
I$
Load
Instr 1
Instr 2
Instr 3
Instr 4
ALU
I$
Reg
D$
Reg
ALU
I$
Reg
D$
Reg
ALU
I$
Reg
D$
Reg
ALU
Reg
D$
Reg
ALU
I$
Reg
D$
Reg
I
n
s
t
r
O
r
d
e
r
Time (clock cycles)
Trying to read (and maybe write) same memory twice in same clock cycle
Conflict for use of a resource

## Slide 13: 1. Structural Hazards
I$
Load
Instr 1
Instr 2
Instr 3
Instr 4
ALU
I$
Reg
D$
Reg
ALU
I$
Reg
D$
Reg
ALU
I$
Reg
D$
Reg
ALU
Reg
D$
Reg
ALU
I$
Reg
D$
Reg
I
n
s
t
r
O
r
d
e
r
Time (clock cycles)
Can we read and write to registers simultaneously?
Conflict for use of a resource

## Slide 14: Structural Hazard #1: Single Memory
Memory is BIG so implemented efficiently (EECS 151)
  Physically cannot perform two reads or a read and a write simultaneously
  Load/Store requires memory access for data; all code need memory access for the instructions
  also a hazard for single-cycle CPU!
Pipelined CPU could solve by stalling: Instruction fetch would have to wait one cycle (Causes pipeline “bubble”)
Solution: Separate instruction/data memories

## Slide 15: Instruction and Data Caches
Caches -- small and fast “buffer” memory

## Slide 16: Structural Hazard #1: Single Memory
Memory is BIG so implemented efficiently (EECS 151)
  Physically cannot perform two reads or a read and a write simultaneously
  Load/Store requires memory access for data; all code need memory access for the instructions
  also a hazard for single-cycle CPU!
Pipelined CPU could solve by stalling: Instruction fetch would have to wait one cycle (Causes pipeline “bubble”)
Solution: Separate instruction/data memories
  Separate L1 I$ and L1 D$ take care of this

## Slide 17: Structural Hazard #2: Registers
Two alternate solutions:
  Build RegFile with independent read and write ports (what you will do in the project; good for single-stage)

## Slide 18
Instr | Instr fetch | Register read | ALU op | Memory access | Register write | Total time
lw | 200ps | 100 ps | 200ps | 200ps | 100 ps | 800ps

## Slide 19: Structural Hazard #2: Registers
Two alternate solutions:
  Build RegFile with independent read and write ports (what you will do in the project; good for single-stage)
  Double Pumping: split RegFile access in two! Prepare to write during 1st half, write on falling edge, read during 2nd half of each clock cycle
    Will save us a cycle later...
    Possible because RegFile access is VERY fast (takes less than half the time of ALU stage)
Conclusion: Read and Write to registers during same clock cycle is okay

## Slide 20: Agenda
Structural Hazards
Data Hazards
  Forwarding
Administrivia
Data Hazards (Continued)
  Load Delay Slot
Control Hazards
  Branch and Jump Delay Slots
  Branch Prediction

## Slide 21: 2. Data Hazards (1/2)
Consider the following sequence of instructions:
add $t0, $t1, $t2
sub $t4, $t0, $t3
and $t5, $t0, $t6
or $t7, $t0, $t8
xor $t9, $t0, $t10
Stored
during WB
Read during ID

## Slide 22: 2. Data Hazards (2/2)
Data-flow backward in time are hazards
sub $t4,$t0,$t3
ALU
I$
Reg
D$
Reg
and $t5,$t0,$t6
ALU
I$
Reg
D$
Reg
or $t7,$t0,$t8
I$
ALU
Reg
D$
Reg
xor $t9,$t0,$t10
ALU
I$
Reg
D$
Reg
add $t0,$t1,$t2
IF
ID/RF
EX
MEM
WB
ALU
I$
Reg
D$
Reg
I
n
s
t
r
O
r
d
e
r
Time (clock cycles)
Hazard if no double pumping

## Slide 23: Data Hazard Solution: Forwarding
Forward result as soon as it is available
  OK that it’s not stored in RegFile yet
sub $t4,$t0,$t3
ALU
I$
Reg
D$
Reg
and $t5,$t0,$t6
ALU
I$
Reg
D$
Reg
or $t7,$t0,$t8
I$
ALU
Reg
D$
Reg
xor $t9,$t0,$t10
ALU
I$
Reg
D$
Reg
add $t0,$t1,$t2
IF
ID/RF
EX
MEM
WB
ALU
I$
Reg
D$
Reg
Arithmetic result
available in EX

## Slide 24: Datapath for Forwarding (1/2)
What changes need to be made here?

## Slide 25: Datapath for Forwarding (2/2)
Handled by forwarding unit
  Pictured: ALU → ALU in one and 2 cycles
Notes: Scan figure 4.54 on p. 368.

## Slide 26: Agenda
Structural Hazards
Data Hazards
  Forwarding
Administrivia
Data Hazards (Continued)
  Load Delay Slot
Control Hazards
  Branch and Jump Delay Slots
  Branch Prediction

## Slide 27: Administrivia
Midterm Grades Released! Regrade requests due Monday, 7/17
  We have received multiple regrade requests that were not well-thought out. Please be considerate!
HW4 due tomorrow
Proj2-2 due Monday, 7/17
Steven’s OH: 511 Soda 11-1 F

## Slide 28: Agenda
Structural Hazards
Data Hazards
  Forwarding
Administrivia
Data Hazards (Continued)
  Load Delay Slot
Control Hazards
  Branch and Jump Delay Slots
  Branch Prediction

## Slide 29: Data Hazard: Loads (1/4)
Recall: Dataflow backwards in time are hazards
Can’t solve all cases with forwarding
  Must stall instruction dependent on load, then forward (more hardware)
sub $t3,$t0,$t2
ALU
I$
Reg
D$
Reg
lw $t0,0($t1)
IF
ID/RF
EX
MEM
WB
ALU
I$
Reg
D$
Reg

## Slide 30: Data Hazard: Loads (2/4)
Hardware stalls pipeline
  Called “hardware interlock”
sub $t3,$t0,$t2
ALU
I$
Reg
D$
Reg
bubble
and $t5,$t0,$t4
ALU
I$
Reg
D$
Reg
bubble
or $t7,$t0,$t6
I$
ALU
Reg
D$
bubble
lw $t0, 0($t1)
IF
ID/RF
EX
MEM
WB
ALU
I$
Reg
D$
Reg
This is what happens in hardware in a “hardware interlock”
Must stall entire pipeline

## Slide 31: Data Hazard: Loads (3/4)
Stall is equivalent to nop
sub $t3,$t0,$t2
and $t5,$t0,$t4
or $t7,$t0,$t6
I$
ALU
Reg
D$
lw $t0, 0($t1)
ALU
I$
Reg
D$
Reg
bubble
bubble
bubble
bubble
bubble
ALU
I$
Reg
D$
Reg
ALU
I$
Reg
D$
Reg
nop

## Slide 32: Data Hazard: Loads (4/4)
Slot after a load is called a load delay slot
  SOME HARDWARE IMPLEMENTATIONS:
    Detect that an instruction uses the result of the load
    stall it for one cycle
  equivalent to a nop between the cycles
Idea: Let the assembler put an unrelated instruction in that slot → no stall!

## Slide 33: Code Scheduling to Avoid Stalls Assembler Update!
Reorder code to avoid use of load result in the next instruction!
MIPS code for D=A+B; E=A+C;
# Method 1:
lw $t1, 0($t0)
lw $t2, 4($t0)
add $t3, $t1, $t2
sw $t3, 12($t0)
lw $t4, 8($t0)
add $t5, $t1, $t4
sw $t5, 16($t0)
# Method 2:
lw $t1, 0($t0)
lw $t2, 4($t0)
lw $t4, 8($t0)
add $t3, $t1, $t2
sw $t3, 12($t0)
add $t5, $t1, $t4
sw $t5, 16($t0)
Stall!
Stall!
13 cycles
11 cycles

## Slide 34: Agenda
Structural Hazards
Data Hazards
  Forwarding
Administrivia
Data Hazards (Continued)
  Load Delay Slot
Control Hazards
  Branch and Jump Delay Slots
  Branch Prediction

## Slide 35: 3. Control Hazards
Branch (beq, bne) determines flow of control
  Fetching next instruction depends on branch outcome
  Pipeline can’t always fetch correct instruction
    Still working on ID stage of branch
Simple Solution: Stall on every branch until we have the new PC value
  How long must we stall?

## Slide 36: Branch Stall
When is comparison result available?
I$
beq
Instr 1
Instr 2
Instr 3
Instr 4
ALU
I$
Reg
D$
Reg
ALU
I$
Reg
D$
Reg
ALU
I$
Reg
D$
Reg
ALU
Reg
D$
Reg
ALU
I$
Reg
D$
Reg
I
n
s
t
r
O
r
d
e
r
Time (clock cycles)
TWO bubbles required per branch!

## Slide 37: 3. Control Hazard: Branching
Option #1: Insert special branch comparator in ID stage
  As soon as instruction is decoded, immediately make a decision and set the new value of the PC
  Benefit: Branch decision made in 2nd stage, so only one nop is needed instead of two
  Side Note: This means that branches are idle in EX, MEM, and WB

## Slide 38: Improved Branch Stall
When is comparison result available?
I$
beq
Instr 1
Instr 2
Instr 3
Instr 4
ALU
I$
Reg
D$
Reg
ALU
I$
Reg
D$
Reg
ALU
I$
Reg
D$
Reg
ALU
Reg
D$
Reg
ALU
I$
Reg
D$
Reg
I
n
s
t
r
O
r
d
e
r
Time (clock cycles)
Only one bubble required now

## Slide 39: Datapath for ID Branch Comparator
What changes need to be made here?

## Slide 40: Data Hazard: Branches!
Recall: Dataflow backwards in time are hazards
Can’t solve all cases with forwarding
  Must stall instruction dependent on load, then forward (more hardware)
beq $0,$t0,foo
ALU
I$
Reg
D$
Reg
add $t0,$t0,$t1
IF
ID/RF
EX
MEM
WB
ALU
I$
Reg
D$
Reg

## Slide 41: 3. Control Hazard: Branching
Option #2: Branch Prediction – guess outcome of a branch, fix afterwards if necessary
  Must cancel (flush) all instructions in pipeline that depended on guess that was wrong
  How many instructions do we end up flushing?
Achieve simplest hardware if we predict that all branches are NOT taken

## Slide 42: 3. Control Hazard: Branching
Option #3: Branch delay slot
  Whether or not we take the branch, always execute the instruction immediately following the branch
  Worst-Case: Put a nop in the branch-delay slot
  Better Case: Move an instruction from before the branch into the branch-delay slot
    Must not affect the logic of program

## Slide 43: 3. Control Hazard: Branching
MIPS uses this delayed branch concept
  Re-ordering instructions is a common way to speed up programs
  Compiler finds an instruction to put in the branch delay slot ≈ 50% of the time
Jumps also have a delay slot
  Why is one needed?

## Slide 44: Delayed Branch Example
add $1, $2, $3
sub $4, $5, $6
beq $1, $4, Exit
or $8, $9, $10
xor $10, $1, $11
Nondelayed Branch
add $1, $2,$3
sub $4, $5, $6
beq $1, $4, Exit
or $8, $9, $10
xor $10, $1, $11
Delayed Branch
Exit:
Exit:
Why not any of the other instructions?

## Slide 45: Delayed Jump in MIPS
MIPS Green Sheet for jal: R[31]=PC+8; PC=JumpAddr
  PC+8 because of jump delay slot!
  Instruction at PC+4 always gets executed before jal jumps to label, so return to PC+8

## Slide 46: Meet The $taff
 | Nikhil | Nick
Spirit Creature | Ostrich | Cookie Monster
All-time Favorite Meme | Covfefe ¦ All Pepes ¦ Fefes | Arthur
What wild thing would you do with 1 million dollars? | Pay off loans & -Fidget spinners or a rap group | Curse people out & afford the lawsuits
Favorite Villian? | Madara ¦ Light from Death Note ¦ Count of Montechristo | Eric Cartman

## Slide 47: Agenda
Structural Hazards
Data Hazards
  Forwarding
Administrivia
Data Hazards (Continued)
  Load Delay Slot
Control Hazards
  Branch and Jump Delay Slots
  Branch Prediction

## Slide 48: Dynamic Branch Prediction
Branch penalty is more significant in deeper pipelines
Use dynamic branch prediction
  Have branch prediction buffer (a.k.a. branch history table) that stores outcomes (taken/not taken) indexed by recent branch instruction addresses
  To execute a branch
    Check table and predict the same outcome for next fetch
    If wrong, flush pipeline and flip prediction

## Slide 49: 1-Bit Predictor: Shortcoming
Examine the code below, assuming both loops will be executed multiple times:
outer: … … inner: …
…
beq …, …, inner … beq …, …, outer
Inner loop branches are predicted wrong twice!
  Predict as taken on last iteration of inner loop
  Then predict as not taken on first iteration of inner loop next time around

## Slide 50
Question: For each code sequences below, choose one of the statements below:
No stalls as is
A
No stalls with forwarding
B
Must stall
C
1: lw $t0,0($t0) add $t1,$t0,$t0 | 2: add $t1,$t0,$t0 addi $t2,$t0,5 addi $t4,$t1,5 | 3: addi $t1,$t0,1 addi $t2,$t0,2 addi $t3,$t0,2 addi $t3,$t0,4 addi $t5,$t1,5

## Slide 51: Code Sequence 1
I$
lw
add
instr
instr
instr
ALU
I$
Reg
D$
Reg
ALU
I$
Reg
D$
Reg
ALU
I$
Reg
D$
Reg
ALU
Reg
D$
Reg
ALU
I$
Reg
D$
Reg
I
n
s
t
r
O
r
d
e
r
Time (clock cycles)
Must stall

## Slide 52: Code Sequence 2
I$
add
addi
addi
instr
instr
ALU
I$
Reg
D$
Reg
ALU
I$
Reg
D$
Reg
ALU
I$
Reg
D$
Reg
ALU
Reg
D$
Reg
ALU
I$
Reg
D$
Reg
I
n
s
t
r
O
r
d
e
r
Time (clock cycles)
forwarding
no forwarding
No stalls with forwarding

## Slide 53: Code Sequence 3
I$
addi
addi
addi
addi
addi
ALU
I$
Reg
D$
Reg
ALU
I$
Reg
D$
Reg
ALU
I$
Reg
D$
Reg
ALU
Reg
D$
Reg
ALU
I$
Reg
D$
Reg
I
n
s
t
r
O
r
d
e
r
Time (clock cycles)
No stalls as is

## Slide 54: Summary
Hazards reduce effectiveness of pipelining
  Cause stalls/bubbles
Structural Hazards
  Conflict in use of datapath component
Data Hazards
  Need to wait for result of a previous instruction
Control Hazards
  Address of next instruction uncertain/unknown
  Branch and jump delay slots