## Slide 1: Direct-Mapped and Set Associative Caches
Instructor: Steven Ho

## Slide 2: Great Idea #3: Principle of Locality/ Memory Hierarchy

## Slide 3: Extended Review of Last Lecture
Why have caches?
  Intermediate level between CPU and memory
  In-between in size, cost, and speed
Memory (hierarchy, organization, structures) set up to exploit temporal and spatial locality
  Temporal: If accessed, will access again soon
  Spatial: If accessed, will access others around it
Caches hold a subset of memory (in blocks)
  We are studying how they are designed for fast and efficient operation (lookup, access, storage)

## Slide 4: Extended Review of Last Lecture
Fully Associative Caches:
  Every block can go in any slot
    Use random or LRU replacement policy when cache full
  Memory address breakdown (on request)
    Tag field is unique identifier (which block is currently in slot)
    Offset field indexes into block (by bytes)
  Each cache slot holds block data, tag, valid bit, and dirty bit (dirty bit is only for write-back)
    The whole cache maintains LRU bits

## Slide 5: Extended Review of Last Lecture
On memory access (read or write):
  Look at ALL cache slots in parallel
  If Valid bit is 0, then ignore (garbage)
  If Valid bit is 1 and Tag matches, then use that data
On write, set Dirty bit if write-back

## Slide 6: Extended Review of Last Lecture
Fully associative cache layout in our example
  6-bit address space, 16-byte cache with 4-byte blocks
  How many blocks do we have? C/K = 4 blocks
  LRU replacement (2 bits), write-back and write allocate
  Offset – 2 bits, Tag – 4 bits
Since this is write back, we’ll need a dirty bit
V | D | Tag | 00 | 01 | 10 | 11
X | X | XXXX | 0x?? | 0x?? | 0x?? | 0x??
X | X | XXXX | 0x?? | 0x?? | 0x?? | 0x??
X | X | XXXX | 0x?? | 0x?? | 0x?? | 0x??
X | X | XXXX | 0x?? | 0x?? | 0x?? | 0x??
Offset
Slot
0
1
2
3
cache size (C)
block size (K)
26 = 64 B address space
Need dirty bit
LRU
XX
LRU bits
V | Tag | 00 | 01 | 10 | 11
X | XXXX | 0x?? | 0x?? | 0x?? | 0x??
X | XXXX | 0x?? | 0x?? | 0x?? | 0x??
X | XXXX | 0x?? | 0x?? | 0x?? | 0x??
X | XXXX | 0x?? | 0x?? | 0x?? | 0x??
Yesterday’s example was write through and looked like this

## Slide 7: FA Cache Examples (3/4)
Consider the following addresses being requested:
  0 2 2 0 16 20 8 4
0
2
miss
hit
Starting with a cold cache:
1 | 0000 | M[0] | M[1] | M[2] | M[3]
0 | 0000 | 0x?? | 0x?? | 0x?? | 0x??
0 | 0000 | 0x?? | 0x?? | 0x?? | 0x??
0 | 0000 | 0x?? | 0x?? | 0x?? | 0x??
1 | 0000 | M[0] | M[1] | M[2] | M[3]
0 | 0000 | 0x?? | 0x?? | 0x?? | 0x??
0 | 0000 | 0x?? | 0x?? | 0x?? | 0x??
0 | 0000 | 0x?? | 0x?? | 0x?? | 0x??
1 | 0000 | M[0] | M[1] | M[2] | M[3]
0 | 0000 | 0x?? | 0x?? | 0x?? | 0x??
0 | 0000 | 0x?? | 0x?? | 0x?? | 0x??
0 | 0000 | 0x?? | 0x?? | 0x?? | 0x??
2
hit
1 | 0000 | M[0] | M[1] | M[2] | M[3]
0 | 0000 | 0x?? | 0x?? | 0x?? | 0x??
0 | 0000 | 0x?? | 0x?? | 0x?? | 0x??
0 | 0000 | 0x?? | 0x?? | 0x?? | 0x??
0
hit
000000
000010
000000
000010

## Slide 8: FA Cache Examples (3/4)
1 | 0000 | M[0] | M[1] | M[2] | M[3]
1 | 0100 | M[16] | M[17] | M[18] | M[19]
1 | 0101 | M[20] | M[21] | M[22] | M[23]
1 | 0010 | M[8] | M[9] | M[10] | M[11]
1 | 0000 | M[0] | M[1] | M[2] | M[3]
1 | 0100 | M[16] | M[17] | M[18] | M[19]
1 | 0101 | M[20] | M[21] | M[22] | M[23]
0 | 0000 | 0x?? | 0x?? | 0x?? | 0x??
1 | 0000 | M[0] | M[1] | M[2] | M[3]
1 | 0100 | M[16] | M[17] | M[18] | M[19]
0 | 0000 | 0x?? | 0x?? | 0x?? | 0x??
0 | 0000 | 0x?? | 0x?? | 0x?? | 0x??
Consider the following addresses being requested:
  0 2 2 0 16 20 8 4
16
8
miss
miss
Starting with a cold cache:
  8 requests, 5 misses – ordering matters!
1 | 0000 | M[0] | M[1] | M[2] | M[3]
0 | 0000 | 0x?? | 0x?? | 0x?? | 0x??
0 | 0000 | 0x?? | 0x?? | 0x?? | 0x??
0 | 0000 | 0x?? | 0x?? | 0x?? | 0x??
1 | 0000 | M[0] | M[1] | M[2] | M[3]
1 | 0100 | M[16] | M[17] | M[18] | M[19]
0 | 0000 | 0x?? | 0x?? | 0x?? | 0x??
0 | 0000 | 0x?? | 0x?? | 0x?? | 0x??
1 | 0000 | M[0] | M[1] | M[2] | M[3]
1 | 0100 | M[16] | M[17] | M[18] | M[19]
1 | 0101 | M[20] | M[21] | M[22] | M[23]
0 | 0000 | 0x?? | 0x?? | 0x?? | 0x??
1 | 0000 | M[0] | M[1] | M[2] | M[3]
1 | 0100 | M[16] | M[17] | M[18] | M[19]
1 | 0101 | M[20] | M[21] | M[22] | M[23]
1 | 0010 | M[8] | M[9] | M[10] | M[11]
20
miss
1 | 0000 | M[0] | M[1] | M[2] | M[3]
1 | 0100 | M[16] | M[17] | M[18] | M[19]
1 | 0101 | M[20] | M[21] | M[22] | M[23]
1 | 0010 | M[8] | M[9] | M[10] | M[11]
4
miss
M H H H
010000
010100
000100
001000
Notes: Extra for experts:
Rearrange the same requests so that there are 5 misses and the final tags are (from top to bottom) 0b0000, 0b0011, 0b0001, 0b0100.
Is it possible for this same set of requests to produce fewer than 5 misses?

## Slide 9: FA Cache Examples (4/4)
Original sequence, but double block size to 8B
  0 2 4 8 20 16 0 2
0
miss
Starting with a cold cache:
0 | 000 | 0x?? | 0x?? | 0x?? | 0x?? | 0x?? | 0x?? | 0x?? | 0x??
0 | 000 | 0x?? | 0x?? | 0x?? | 0x?? | 0x?? | 0x?? | 0x?? | 0x??
1 | 000 | M[0] | M[1] | M[2] | M[3] | M[4] | M[5] | M[6] | M[7]
0 | 000 | 0x?? | 0x?? | 0x?? | 0x?? | 0x?? | 0x?? | 0x?? | 0x??
1 | 000 | M[0] | M[1] | M[2] | M[3] | M[4] | M[5] | M[6] | M[7]
0 | 000 | 0x?? | 0x?? | 0x?? | 0x?? | 0x?? | 0x?? | 0x?? | 0x??
1 | 000 | M[0] | M[1] | M[2] | M[3] | M[4] | M[5] | M[6] | M[7]
0 | 000 | 0x?? | 0x?? | 0x?? | 0x?? | 0x?? | 0x?? | 0x?? | 0x??
2
4
hit
hit
8
miss
1 | 000 | M[0] | M[1] | M[2] | M[3] | M[4] | M[5] | M[6] | M[7]
0 | 000 | 0x?? | 0x?? | 0x?? | 0x?? | 0x?? | 0x?? | 0x?? | 0x??
1 | 000 | M[0] | M[1] | M[2] | M[3] | M[4] | M[5] | M[6] | M[7]
1 | 001 | M[8] | M[9] | M[10] | M[11] | M[12] | M[13] | M[14] | M[15]
000000
000010
000100
001000

## Slide 10: FA Cache Examples (4/4)
Original sequence, but double block size
  0 2 4 8 20 16 0 2
20
miss
Starting with a cold cache:
1 | 000 | M[0] | M[1] | M[2] | M[3] | M[4] | M[5] | M[6] | M[7]
1 | 001 | M[8] | M[9] | M[10] | M[11] | M[12] | M[13] | M[14] | M[15]
1 | 010 | M[16] | M[17] | M[18] | M[19] | M[20] | M[21] | M[22] | M[23]
1 | 001 | M[8] | M[9] | M[10] | M[11] | M[12] | M[13] | M[14] | M[15]
1 | 010 | M[16] | M[17] | M[18] | M[19] | M[20] | M[21] | M[22] | M[23]
1 | 000 | M[0] | M[1] | M[2] | M[3] | M[4] | M[5] | M[6] | M[7]
16
0
hit
miss
1 | 010 | M[16] | M[17] | M[18] | M[19] | M[20] | M[21] | M[22] | M[23]
1 | 001 | M[8] | M[9] | M[10] | M[11] | M[12] | M[13] | M[14] | M[15]
2
hit
  8 requests, 4 misses – cache parameters matter!
M H H M
010100
010000
000000
000010

## Slide 11
Question:
Starting with the same cold cache as the first 3 examples, which of the sequences below will result in the final state of the cache shown here:
0 2 12 4 16 8 0 6
(A)
0 8 4 16 0 12 6 2
(B)
6 12 4 8 2 16 0 0
(C)
2 8 0 4 6 16 12 0
(D)
1 | 0000 | M[0] | M[1] | M[2] | M[3]
1 | 0011 | M[12] | M[13] | M[14] | M[15]
1 | 0001 | M[4] | M[5] | M[6] | M[7]
1 | 0100 | M[16] | M[17] | M[18] | M[19]
LRU
10
0
1
2
3

## Slide 12
Question:
Starting with the same cold cache as the first 3 examples, which of the sequences below will result in the final state of the cache shown here:
0 2 12 4 16 8 0 6
(A)
0 8 4 16 0 12 6 2
(B)
6 12 4 8 2 16 0 0
(C)
2 8 0 4 6 16 12 0
(D)
1 | 0000 | M[0] | M[1] | M[2] | M[3]
1 | 0011 | M[12] | M[13] | M[14] | M[15]
1 | 0001 | M[4] | M[5] | M[6] | M[7]
1 | 0100 | M[16] | M[17] | M[18] | M[19]
LRU
10
0
1
2
3

## Slide 13
Question:
Starting with the same cold cache as the first 3 examples, which of the sequences below will result in the final state of the cache shown here:
0 2 12 4 16 8 0 6
(A)
0 8 4 16 0 12 6 2
(B)
6 12 4 8 2 16 0 0
(C)
2 8 0 4 6 16 12 0
(D)
1 | 0000 | M[0] | M[1] | M[2] | M[3]
1 | 0011 | M[12] | M[13] | M[14] | M[15]
1 | 0001 | M[4] | M[5] | M[6] | M[7]
1 | 0100 | M[16] | M[17] | M[18] | M[19]
LRU
10
0
1
2
3

## Slide 14: Memory Accesses
The picture so far:
Cache
Addr
miss
hit
data
CPU
Main Memory

## Slide 15: Handling Write Hits
Write hits (D$)
  Write-Through Policy: Always write data to cache and to memory (through cache)
    Forces cache and memory to always be consistent
    Slow! (every memory access is long)
    Include a Write Buffer that updates memory in parallel with processor
Assume present in all schemes when writing to memory
Notes: In a write-back cache, because we cannot overwrite the block (since we may not have a backup copy anywhere), stores either require two cycles (one to check for a hit, followed by one to actually do the write) or require a write buffer to hold that data (essentially pipelining the write).
By comparison, a write-through cache can always be done in one cycle assuming there is room in the write buffer. Read the tag and write the data in parallel. If the tag doesn’t match, the generate a write miss to fetch the rest of that block from the next level in the hierarchy (and update the tag field).

## Slide 16: Handling Write Hits
Write hits (D$)
  Write-Back Policy: Write data only to cache, then update memory when block is removed
    Allows cache and memory to be inconsistent
    Multiple writes collected in cache; single write to memory per block
    Dirty bit: Extra bit per cache row that is set if block was written to (is “dirty”) and needs to be written back

## Slide 17: Handling Cache Misses
Miss penalty grows as block size does
Read misses (I$ and D$)
  Stall execution, fetch block from memory, put in cache, send requested data to processor, resume
Write misses (D$)
  Always have to update block from memory
  We have to make a choice:
    Carry the updated block into cache or not?
Notes: Write allocate almost always paired with write-back.

## Slide 18: Write Allocate
Write Allocate policy: when we bring the block into the cache after a write miss
No Write Allocate policy: only change main memory after a write miss
  Write allocate almost always paired with write-back
    Eg: Accessing same address many times -> cache it
  No write allocate typically paired with write-through
    Eg: Infrequent/random writes -> don’t bother caching it
Notes: Write allocate almost always paired with write-back.

## Slide 19: Updated Cache Picture
Fully associative, write through
  Same as our simplified examples from before
Fully associative, write back
Write miss procedure (write allocate or not) only affects behavior, not design
V | D | Tag | 00 | 01 | 10 | 11
X | X | XXXX | 0x?? | 0x?? | 0x?? | 0x??
X | X | XXXX | 0x?? | 0x?? | 0x?? | 0x??
X | X | XXXX | 0x?? | 0x?? | 0x?? | 0x??
X | X | XXXX | 0x?? | 0x?? | 0x?? | 0x??
Slot
0
1
2
3
LRU
XX

## Slide 20: How do we use this thing?
Nothing changes from the programmer’s perspective
  Still just issuing lw and sw instructions
The rest is handled in hardware:
  Checking the cache
  Extracting the data using the offset
Why should a programmer care?
  Understanding cache parameters = faster programs

## Slide 21: Agenda
Review of yesterday
Administrativia
Direct-Mapped Caches
Set Associative Caches
Cache Performance

## Slide 22: Administrivia
HW5 due & Proj3-1 due Thursday!
Midterm 2 is Mon 7/31 9:30-11am in 155 Dwinelle again
  Review Session Fri 7/28, 2-4pm in HP Auditorium (306 Soda)
  2 Doubled-sided sheets of notes
  Covers up through Parallel Computing (Next Tuesday’s lecture)

## Slide 23: Direct-Mapped Caches (1/3)
Each memory block is mapped to exactly one slot in the cache (direct-mapped)
  Every block has only one “home”
  Use hash function to determine which slot
Comparison with fully associative
  Check just one slot for a block (faster!)
  No replacement policy necessary
  Access pattern may leave empty slots in cache
Notes:   Check just one location to see if block is in cache.

## Slide 24: Direct-Mapped Caches (2/3)
Offset field remains the same as before
Recall: blocks consist of adjacent bytes
  Do we want adjacent blocks to map to same slot?
  Index field: Apply hash function to block address to determine which slot the block goes in
    (block address) modulo (# of blocks in the cache)
Tag field maintains same function (identifier), but is now shorter

## Slide 25: TIO Address Breakdown
Memory address fields:
Meaning of the field sizes:
  O bits ↔ 2O bytes/block = 2O-2 words/block
  I bits ↔ 2I slots in cache = cache size / block size
  T bits = A – I – O, where A = # of address bits (A = 32 here)
Tag
Index
Offset
31
0
T bits
I bits
O bits

## Slide 26: Direct-Mapped Caches (3/3)
What’s actually in the cache?
  Block of data (8 × K = 8 × 2O bits)
  Tag field of address as identifier (T bits)
  Valid bit (1 bit)
  Dirty bit (1 bit if write-back)
  No replacement management bits!
Total bits in cache = # slots × (8×K + T + 1 + 1) = 2I × (8×2O + T + 1 + 1) bits

## Slide 27: DM Cache Example (1/5)
Cache parameters:
  Direct-mapped, address space of 64B, block size of 4B, cache size of 16B, write-through
TIO Breakdown:
  O = log2(4) = 2
  Cache size / block size = 16/4 = 4, so I = log2(4) = 2
  A = log2(64) = 6 bits, so T = 6 – 2 – 2 = 2
Bits in cache = 22 × (8×22 + 2 + 1) = 140 bits
XX
XX
XX
Memory Addresses:
Block address
Notes: Compare with fully associative example from last lecture. This takes 140 bits to implement instead of 150 bits because of shorter Tag and no LRU bits.

## Slide 28: DM Cache Example (2/5)
Cache parameters:
  Direct-mapped, address space of 64B, block size of 4B, cache size of 16B, write-through
  Offset – 2 bits, Index – 2 bits, Tag – 2 bits
35 bits per index/slot, 140 bits to implement
V | Tag | 00 | 01 | 10 | 11
X | XX | 0x?? | 0x?? | 0x?? | 0x??
X | XX | 0x?? | 0x?? | 0x?? | 0x??
X | XX | 0x?? | 0x?? | 0x?? | 0x??
X | XX | 0x?? | 0x?? | 0x?? | 0x??
Index
00
01
10
11
Offset

## Slide 29: DM Cache Example (3/5)
Main Memory:
Which blocks map to each row of the cache?
(see colors)
On a memory request: (let’s say 001011two)
1) Take Index field (10)
2) Check if Valid bit is true in that row of cache
3) If valid, then check if Tag matches
0000xx
0001xx
0010xx
0011xx
0100xx
0101xx
0110xx
0111xx
1000xx
1001xx
1010xx
1011xx
1100xx
1101xx
1110xx
1111xx
00
01
10
11
Cache:
Tag
Data
Valid
Index
Cache slots exactly match the Index field
Which blocks map to each row of the cache?
(see colors)
Main Memory shown in blocks, so offset bits not shown (x’s)

## Slide 30: DM Cache Example (4/5)
Consider the sequence of memory address accesses
  0 2 4 8 20 16 0 2
0
4
miss
miss
Starting with a cold cache:
0 | 00 | 0x?? | 0x?? | 0x?? | 0x??
0 | 00 | 0x?? | 0x?? | 0x?? | 0x??
0 | 00 | 0x?? | 0x?? | 0x?? | 0x??
0 | 00 | 0x?? | 0x?? | 0x?? | 0x??
1 | 00 | M[0] | M[1] | M[2] | M[3]
0 | 00 | 0x?? | 0x?? | 0x?? | 0x??
0 | 00 | 0x?? | 0x?? | 0x?? | 0x??
0 | 00 | 0x?? | 0x?? | 0x?? | 0x??
1 | 00 | M[0] | M[1] | M[2] | M[3]
0 | 00 | 0x?? | 0x?? | 0x?? | 0x??
0 | 00 | 0x?? | 0x?? | 0x?? | 0x??
0 | 00 | 0x?? | 0x?? | 0x?? | 0x??
1 | 00 | M[0] | M[1] | M[2] | M[3]
0 | 00 | 0x?? | 0x?? | 0x?? | 0x??
0 | 00 | 0x?? | 0x?? | 0x?? | 0x??
0 | 00 | 0x?? | 0x?? | 0x?? | 0x??
2
hit
1 | 00 | M[0] | M[1] | M[2] | M[3]
1 | 00 | M[4] | M[5] | M[6] | M[7]
0 | 00 | 0x?? | 0x?? | 0x?? | 0x??
0 | 00 | 0x?? | 0x?? | 0x?? | 0x??
1 | 00 | M[0] | M[1] | M[2] | M[3]
1 | 00 | M[4] | M[5] | M[6] | M[7]
0 | 00 | 0x?? | 0x?? | 0x?? | 0x??
0 | 00 | 0x?? | 0x?? | 0x?? | 0x??
8
miss
1 | 00 | M[0] | M[1] | M[2] | M[3]
1 | 00 | M[4] | M[5] | M[6] | M[7]
1 | 00 | M[8] | M[9] | M[10] | M[11]
0 | 00 | 0x?? | 0x?? | 0x?? | 0x??
00
01
10
11
00
01
10
11
00
01
10
11
00
01
10
11
000000
000010
001000
000100

## Slide 31: DM Cache Example (5/5)
Consider the sequence of memory address accesses
  0 2 4 8 20 16 0 2
20
0
miss
miss
Starting with a cold cache:
  8 requests, 6 misses – last slot was never used!
1 | 00 | M[0] | M[1] | M[2] | M[3]
1 | 00 | M[4] | M[5] | M[6] | M[7]
1 | 00 | M[8] | M[9] | M[10] | M[11]
0 | 00 | 0x?? | 0x?? | 0x?? | 0x??
1 | 00 | M[0] | M[1] | M[2] | M[3]
1 | 01 | M[20] | M[21] | M[22] | M[23]
1 | 00 | M[8] | M[9] | M[10] | M[11]
0 | 00 | 0x?? | 0x?? | 0x?? | 0x??
1 | 01 | M[16] | M[17] | M[18] | M[19]
1 | 01 | M[20] | M[21] | M[22] | M[23]
1 | 00 | M[8] | M[9] | M[10] | M[11]
0 | 00 | 0x?? | 0x?? | 0x?? | 0x??
16
miss
1 | 00 | M[0] | M[1] | M[2] | M[3]
1 | 01 | M[20] | M[21] | M[22] | M[23]
1 | 00 | M[8] | M[9] | M[10] | M[11]
0 | 00 | 0x?? | 0x?? | 0x?? | 0x??
2
hit
00
01
10
11
00
01
10
11
00
01
10
11
00
01
10
11
010100
010000
000010
000000

## Slide 32: Worst-Case for Direct-Mapped
Cold DM $ that holds four 1-word blocks
Consider the memory accesses: 0, 16, 0, 16,...
000000 010000 000000
HR of 0%
  Ping pong effect: alternating requests that map into the same cache slot
Does fully associative have this problem?
0
16
0
Miss
Miss
Miss
00 M[0-3]
00 M[0-3]
01 M[16-19]
. . .

## Slide 33: Comparison So Far
Fully associative
  Block can go into any slot
  Must check ALL cache slots on request (“slow”)
  TO breakdown (i.e. I = 0 bits)
  “Worst case” still fills cache (more efficient)
Direct-mapped
  Block goes into one specific slot (set by Index field)
  Only check ONE cache slot on request (“fast”)
  TIO breakdown
  “Worst case” may only use 1 slot (less efficient)

## Slide 34: Meet The $taff
 | Rebecca | Steven
Go-to phone app | Duolingo | Pokemon Go
Catch Phrase | ANOTHER MUX!!! | cool beanz, rad sauce
Spirit Emoji | (cache, not cash) | 💁, 💩, 🙅
Binge Show | The Good Place | Bob's Burgers

## Slide 35: Agenda
Review of yesterday
Administrivia
Direct-Mapped Caches
Set Associative Caches
Cache Performance

## Slide 36: Set Associative Caches
Compromise!
  More flexible than DM, more structured than FA
N-way set-associative: Divide $ into sets, each of which consists of N slots
  Memory block maps to a set determined by Index field and is placed in any of the N slots of that set
  Call N the associativity
  New hash function: (block address) modulo (# sets in the cache)
  Replacement policy applies to every set
Notes: All of the tags of all of the elements of the set must be searched for a match.

## Slide 37: Effect of Associativity on TIO (1/2)
Here we assume a cache of fixed size (C)
Offset: # of bytes in a block (same as before)
Index: Instead of pointing to a slot, now points to a set, so I = log2(C÷K÷N)
  Fully associative (1 set): 0 Index bits!
  Direct-mapped (N = 1): max Index bits
  Set associative: somewhere in-between
Tag: Remaining identifier bits (T = A – I – O)
Notes: C = cache size, B = block size

## Slide 38: Effect of Associativity on TIO (2/2)
For a fixed-size cache, each increase by a factor of two in associativity doubles the number of blocks per set (i.e. the number of slots) and halves the number of sets – decreasing the size of the Index by 1 bit and increasing the size of the Tag by 1 bit
Block offset
Byte offset
Index
Tag
Decreasing associativity
Fully associative
(only one set)
Direct mapped
(only one way)
Increasing associativity
Selects the set
Used for tag comparison
Selects the word in the block
Notes: For lecture
In 2008, the greater size and power consumption of CAMs generally leads to 2-way and 4-way set associativity being built from standard SRAMs with comparators with 8-way and above being built using CAMs

## Slide 39: Example: Eight-Block Cache Configs
Total size of $ = # sets × associativity
For fixed $ size, associativity ↑ means # sets ↓ and slots per set ↑
With 8 blocks, an 8-way set associative $ is same as a fully associative $

## Slide 40: Block Placement Schemes
Place memory block 12 in a cache that holds 8 blocks
Fully associative: Can go in any of the slots (all 1 set)
Direct-mapped: Can only go in slot (12 mod 8) = 4
2-way set associative: Can go in either slot of set (12 mod 4) = 0

## Slide 41: SA Cache Example (1/5)
Cache parameters:
  2-way set associative, 6-bit addresses, 1-word blocks, 4-word cache, write-through
How many sets?
  C÷K÷N = 4÷1÷2 = 2 sets
TIO Breakdown:
  O = log2(4) = 2, I = log2(2) = 1, T = 6 – 1 – 2 = 3
XXX
X
XX
Memory Addresses:
Block address

## Slide 42: SA Cache Example (2/5)
Cache parameters:
  2-way set associative, 6-bit addresses, 1-word blocks, 4-word cache, write-through
  Offset – 2 bits, Index – 1 bit, Tag – 3 bits
37 bits per slot, 37*2 = 74 bits per set, 2*74 = 148 bits to implement
V | Tag | 00 | 01 | 10 | 11
X | XXX | 0x?? | 0x?? | 0x?? | 0x??
X | XXX | 0x?? | 0x?? | 0x?? | 0x??
X | XXX | 0x?? | 0x?? | 0x?? | 0x??
X | XXX | 0x?? | 0x?? | 0x?? | 0x??
Index
 | 0
 | 1
 | 0
 | 1
Offset
0
1
LRU
X
LRU
X

## Slide 43: SA Cache Example (3/5)
0000xx
0001xx
0010xx
0011xx
0100xx
0101xx
0110xx
0111xx
1000xx
1001xx
1010xx
1011xx
1100xx
1101xx
1110xx
1111xx
0
Cache:
Tag
Data
V
Slot
1
0
1
Set
0
1
Main Memory:
Each block maps into one set (either slot)
(see colors)
On a memory request: (let’s say 001011two)
1) Take Index field (0)
2) For EACH slot in set,
check valid bit,
then compare Tag
Set numbers exactly match the Index field
Main Memory shown in blocks, so offset bits not shown (x’s)

## Slide 44: SA Cache Example (4/5)
Consider the sequence of memory address accesses
  0 2 4 8 20 16 0 2
0
4
miss
miss
Starting with a cold cache:
0 | 000 | 0x?? | 0x?? | 0x?? | 0x??
0 | 000 | 0x?? | 0x?? | 0x?? | 0x??
0 | 000 | 0x?? | 0x?? | 0x?? | 0x??
0 | 000 | 0x?? | 0x?? | 0x?? | 0x??
1 | 000 | M[0] | M[1] | M[2] | M[3]
0 | 000 | 0x?? | 0x?? | 0x?? | 0x??
0 | 000 | 0x?? | 0x?? | 0x?? | 0x??
0 | 000 | 0x?? | 0x?? | 0x?? | 0x??
1 | 000 | M[0] | M[1] | M[2] | M[3]
0 | 000 | 0x?? | 0x?? | 0x?? | 0x??
0 | 000 | 0x?? | 0x?? | 0x?? | 0x??
0 | 000 | 0x?? | 0x?? | 0x?? | 0x??
1 | 000 | M[0] | M[1] | M[2] | M[3]
0 | 000 | 0x?? | 0x?? | 0x?? | 0x??
0 | 000 | 0x?? | 0x?? | 0x?? | 0x??
0 | 000 | 0x?? | 0x?? | 0x?? | 0x??
2
hit
1 | 000 | M[0] | M[1] | M[2] | M[3]
0 | 000 | 0x?? | 0x?? | 0x?? | 0x??
1 | 000 | M[4] | M[5] | M[6] | M[7]
0 | 000 | 0x?? | 0x?? | 0x?? | 0x??
1 | 000 | M[0] | M[1] | M[2] | M[3]
0 | 000 | 0x?? | 0x?? | 0x?? | 0x??
1 | 000 | M[4] | M[5] | M[6] | M[7]
0 | 000 | 0x?? | 0x?? | 0x?? | 0x??
8
miss
1 | 000 | M[0] | M[1] | M[2] | M[3]
1 | 001 | M[8] | M[9] | M[10] | M[11]
1 | 000 | M[4] | M[5] | M[6] | M[7]
0 | 000 | 0x?? | 0x?? | 0x?? | 0x??
0
1
0
1
0
1
0
1
0
1
0
1
0
1
0
1
0
1
0
1
0
1
0
1
000000
000010
001000
000100

## Slide 45: SA Cache Example (5/5)
Consider the sequence of memory address accesses
  0 2 4 8 20 16 0 2
20
0
miss
miss
Starting with a cold cache:
  8 requests, 6 misses
1 | 000 | M[0] | M[1] | M[2] | M[3]
1 | 001 | M[8] | M[9] | M[10] | M[11]
1 | 000 | M[4] | M[5] | M[6] | M[7]
0 | 000 | 0x?? | 0x?? | 0x?? | 0x??
1 | 000 | M[0] | M[1] | M[2] | M[3]
1 | 001 | M[8] | M[9] | M[10] | M[11]
1 | 000 | M[4] | M[5] | M[6] | M[7]
1 | 010 | M[20] | M[21] | M[22] | M[23]
1 | 010 | M[16] | M[17] | M[18] | M[19]
1 | 001 | M[8] | M[9] | M[10] | M[11]
1 | 000 | M[4] | M[5] | M[6] | M[7]
1 | 010 | M[20] | M[21] | M[22] | M[23]
16
miss
1 | 010 | M[16] | M[17] | M[18] | M[19]
1 | 000 | M[0] | M[1] | M[2] | M[3]
1 | 000 | M[4] | M[5] | M[6] | M[7]
1 | 010 | M[20] | M[21] | M[22] | M[23]
2
hit
0
1
0
1
0
1
0
1
0
1
0
1
0
1
0
1
0
1
0
1
0
1
0
1
1 | 000 | M[0] | M[1] | M[2] | M[3]
1 | 001 | M[8] | M[9] | M[10] | M[11]
1 | 000 | M[4] | M[5] | M[6] | M[7]
1 | 010 | M[20] | M[21] | M[22] | M[23]
M H M M
010100
010000
000010
000000

## Slide 46: Worst Case for Set Associative
Worst case for DM was repeating pattern of 2 into same cache slot (HR = 0/n)
  Set associative for N > 1: HR = (n-2)/n
Worst case for N-way SA with LRU?
  Repeating pattern of at least N+1 that maps into same set
  Back to HR = 0:
000 M[0-3]
001 M[8-11]
0, 8, 16, 0, 8, …
M
M
M
010 M[16-19]
000 M[0-3]
M
001 M[8-11]
M
Notes: For lecture
Another sample string to try 0 1 2 3 0 8 11 0 3

## Slide 47
Question: What is the TIO breakdown for the following cache?
32-bit address space
32 KiB 4-way set associative cache
8 word blocks
A = 32, C = 32 KiB = 215 B, N = 4, K = 8 words = 32 B
21 8 3
(A)
19 8 5
(B)
19 10 3
(C)
17 10 5
(D)
T I O
O = log2(K) = 5 bits
C/K = 210 slots
C/K/N = 28 sets
I = log2(C/K/N) = 8 bits
T = A – I – O = 19 bits

## Slide 48: Summary
Set associativity determines flexibility of block placement
  Fully associative: blocks can go anywhere
  Direct-mapped: blocks go in one specific location
  N-way: cache split into sets, each of which have n slots to place memory blocks